        AI-Driven Morse Code
        Translation System
Subject: ELECTRONICS AND ELECTRICAL ENGINEERING
Institution: Amrita University
Presented By:
-AAKASH G S (CB.SC.U4AIE24101)
-NEERAJ T (CB.SC.U4AIE24141)
-NITHIN AARYA(CB.SC.U4AIE24142)
-PUNEETH KUMAR KALINGA
(CB.SC.U4AIE24146)

---
Contents
1. Introduction
2. Objectives
3. Components
4. Connection overview
5. Methodology
6. Software and code implementation
7. Results and Features
8. Future Scope
9. References

---
introduction
Morse Code is a method of encoding text using dots and dashes.​
Our project uses AI and Arduino to translate Morse Code into text and display it on an LCD screen.​
Input methods: Sound, Button (Manual).​

---
Objectives
- To develop a user-friendly web-based interface for Morse code translation.
- To implement real-time translation between text and Morse code.
- To integrate hardware (LCD & buzzer) for visual and auditory Morse signals.
- To ensure accurate and efficient Morse decoding through Arduino processing.

---
COMPONENTS:
Arduino Uno – Main microcontroller for processing Morse Code input.
16x2 LCD Display – Shows the translated text.
Push Buttons – For manual Morse Code input.
Buzzer-used to generate sound (beep)
I2C module - I2C (Inter-Integrated Circuit) is a communication protocol that allows two devices to communicate with each other using only two wires.
SDA (Serial Data Line) → Transfers the data
SCL (Serial Clock Line) → Synchronizes the data transfer
Power Source – USB or external power supply.

---
CONNECTION OVERVIEW
I2C to Arduino UNO : Connecting the SCL and SDA of I2C to Analog pins A5 and A4 of Arduino and we are connecting VCC to 5V and other pin to ground
Buttons: Connected to digital input pins
Buzzers: Connected to digital and other one to ground
Power Source: Arduino powered via USB or Battery

---
METHODOLOGY:
The methodology of the Morse Code Translator involves using a push button to input Morse Code, where short and long presses represent dots (.) and dashes (-).
The Arduino processes these signals and converts them into Morse Code, triggering a buzzer for audio output.
The I2C module simplifies LCD connectivity, displaying the Morse Code or text in real-time, ensuring efficient and clear communication.

---
Software & Code Implementation
Arduino Code: Reads input from buttons and converts Morse to text.
Arduino IDE is used as the primary software to write, compile, and upload the code to the Arduino UNO microcontroller. The software implementation involves defining Morse Code patterns for each alphabet, number, and special character in the code.
Serial Communication: Sends/receives data between Arduino and AI model.

---
Results and features
- The system successfully translates text to Morse and vice versa.
- The system provides accurate and efficient translation between text and Morse code in real-time..
- Challenges encountered in real-time serial communication, resolved through debugging
   and optimization.

---
Future Scope
Wireless Morse Code Transmission (IoT-based).Integration with mobile apps for real-time translation.
Improved AI-based accuracy using deep learning.

---
References
https://ijarcce.com/papers/morse-code-decoder-using-arduino
https://ieeexplore.ieee.org/document/Morse Code Translator Using the Arduino Platform: Crafting the Future of Microcontrollers

---
Thank
You

---
Literature Review
S. No.	Title	Year	Methodology	Key Contribution
1	Morse Code Recognition (AI)	2019	Neural Networks	Improved accuracy / Morse decoding
2	Arduino-Based Translator	2020	Micro / controller	Real-time signal processing
3	IoT-Based Morse Communication	2021	IoT & Wireless	Remote Morse transmission